## Slide 1: Amplitude Modulation Course Teacher Dr. Monir Morshed Professor, Dept. of ICT Email:monirmorshed.ict@mbstu.ac.bd

## Slide 2
Modulation is a process of varying the characteristics of RF carrier wave in accordance with a modulating signal that typically contains information that is to be transmitted.
The original signal that generated from input transducer which actually we want to sent through transmitter is called Message Signal or modulating Signal or Baseband Signal.
The High Frequency Sinusoidal Signal Which is used to shift the frequency of message signal is called carrier signal.
Modulation
m(t)
Modulating signal
Modulated signal
m(t)cosωct
cosωct
Carrier
Fig. Modulator

## Slide 3
Different types of modulation systems

## Slide 4
Amplitude Modulation
Amplitude Modulation is a process of varying amplitude of high frequency carrier signal in accordance with the instantaneous amplitude of the information signal and also the frequency and phase are kept constant.
If the bandwidth of modulating signal is B Hz, then bandwidth of modulated signal is 2B Hz. The band above fc is USB, and below fc is LSB. Since, modulated signal does not contain discrete component of carrier frequency, it is called double side band suppressed carrier (DSB-SC).

## Slide 5: Demodulation
Demodulator: recovering the message signal at the receiver from the modulated signal.

## Slide 6
General Equation of AM and Spectrum
Let us consider, a sinusoidal carrier wave
Now, if denotes the modulating or baseband signal, according to AM, So, amplitude modulated wave may be expressed as
Where, is called the envelope of the AM wave.

## Slide 7
Modulation Index
In AM wave, the modulation index (m) is defined as
Where, Em and Ec is amplitude of the modulating and carrier waves respectively.
When the modulation index has values between 0 and 1 and no distortion is introduced in the AM wave.
, the modulation index is greater than 1, this will distort the shape of AM signal.
The distortion happens for over modulation.
The modulation index is also called modulation factor.
The modulation index as percentage can be written as:

## Slide 8
Linear and Over Modulation
Based on the values of modulation index, it can be classified as:
          Linear modulation
          Over modulation
Linear Modulation: If or if the percentage modulation is less than 100, then the type of modulation is linear amplitude modulation.
Over modulation: Ifif the percentage modulation is greater than 100%, then the type of modulation is called as over modulation. Over modulation introduces envelope distortion . Therefore, it should be avoided .

## Slide 9
Evaluation of Modulation Index
The modulation index can be measured using the following two methods :
      Using the AM signal as it is
      Using the trapezoidal display of the AM wave
The AM Wave: If we see the AM wave in the cathode ray oscilloscope (CRO), it will appears to be the following figure:
Or,
But,
Hence,

## Slide 10
Using the trapezoidal display of the AM wave
The set up for evaluating the modulation index using trapezoidal display has been shown in the following figures:
Or,
See example 3.2, 3.3, 3.4, 3.5 of SS books.

## Slide 11
Transmission Efficiency
Transmission efficiency of an AM wave is the ratio of the transmitted power which contains the information (i.e. the total sideband power) to the total transmitted power.
The higher percentage of modulation is preferred for strong and more intelligible received signal because it increases the transmitted power Pt by the AM transmitter.

## Slide 12
Single Tone AM
Till now we considered, the baseband signal as a random signal, now let us consider
Let the carrier signal be :
We know that the general expression for AM signal is :
Single-sided frequency spectrum of single-tone AM wave
See example 3.7, 3.3, 3.4, 3.5 of SS books.

## Slide 13
Power Content in AM Wave
We know that the general expression for AM signal is :
The total power of is the sum of carrier power and sideband power
Carrier power,
Sideband Power,
Therefore, total power,
Sideband term
Carrier term only

## Slide 14
Transmission Efficiency of AM Wave
Total modulated power,
The useful message power is carried by the sidebands,
The carrier power, is a waste from transmission point of view because it does not carry any information.
Hence, efficiency of AM wave can be defined as
Transmission efficiency,
The maximum transmission efficiency of AM wave is 33.33%. It means that only one third of total power is carried by sides bands and rest two-third is wasted by carrier.
N.B.: Find the transmission efficiency of single-tone AM wave.

## Slide 15: Type of Modulators
Multiplier Modulators: A variable gain amplifier in which the gain parameter (such as the  of transistor) is controlled by the message signal m(t) and the input is the carrier signal.
      Difficult to maintain linearity in this kind of amplifier
      It is also expensive
Nonlinear Modulators: Nonlinear devices such as diode or transistors are used to output modulated signal.
]-]
Single balanced modulator because one of the input does not appear at the output z(t)

## Slide 16: Type of Modulators
Switching Modulators

## Slide 17: Circuit of Switching Modulators
Diode-bridge electronic switch:
Shunt-bridge diode modulator
Diode-bridge electronic switch
Series-bridge diode modulator
When Vc > Vd all diodes are open and matched
VD1 = VD2
VD1 = Vc – Va
VD2 = Vc – Vb
Va = Vb

## Slide 18: Circuit of Switching Modulators
Ring Modulator
During Positive cycle of carrier:
- D1 & D3 Conducts
- a connected to c & b connected to d
- output proportional to m(t)
During Negative cycle of carrier:
- D2 & D4 Conducts
- a connected to d & b connected to c
- output proportional to -m(t)
Double Balanced Modulator

## Slide 19: Demodulation of DSB-SC Signals
The DSB-SC signal may be demodulated by the following methods:
        Synchronous or coherent detection method
        Using envelope detector after carrier reinsertion
- The received signal might suffer from some unknown frequency or
phase shift.
- The receiver must be sophisticated to generate a local oscillator
cos[(ωc+Δω)t - θd)] purely from the received signal r(t).
Challenge of coherent demodulation for DSB-SC signals
- Amplitude modulation (AM) that transmit the carrier with the modulated
signal will simplify the job of the receiver.

## Slide 20
Synchronous Detection Method
It is a method of DSB-SC detection which is shown in the following figure:
Multiplier
Low pass filter (LPF)
Baseband or modulating signal
, locally generated (carrier signal)
Receiving antenna
,
Modulated or DSB-SC signal
Mathematically, .
When e(t) is passed trhough a LPF,
In frequency spectrum of e(t) using FT as:

## Slide 21: Envelope Detection
Rectifier

## Slide 22: Envelope Detection
RC too large

## Slide 23: Bandwidth-Efficient Amplitude Modulations
Single-Sideband (SSB) modulation, which remove either the LSB or the USB so that for one message signal m(t), there is only a bandwidth of B Hz.
Quadrature Amplitude (QAM) modulation, which utilize spectral redundancy by sending two messages over the same bandwidth, 2B Hz .
The bandwidth of Amplitude Modulation is 2B Hz.
How to reduce bandwidth?

## Slide 24: Amplitude Modulation: Single Sideband (SSB)
Single-Sideband (SSB) modulation, use Hilbert transform to remove the LSB or USB.

## Slide 25: Hilbert Transform
Hilbert Transform
h(t)
H(f)
m(t)
mh(t)
M(f)
Mh(f)
Hilbert transform is an ideal phase shifter that shifts the phase of every positive spectral component by -π/2.

## Slide 26: Time Domain Representation of SSB Signals

## Slide 27: Coherent Demodulation of SSB-SC
These terms can be filtered out by using low-pass filter

## Slide 28: Quadrature Amplitude Modulation (QAM)
It is difficult to generate accurately SSB-SC and requires large power A >>|m(t)|, so QAM offers an attractive alternative.
QAM operates by transmitting two DSB signals via carrier of the same frequency but in phase quadrature.
Transmitter
Receiver

## Slide 29: Quadrature Amplitude Demodulation
In-phase channel
Quadrature channel

## Slide 30: Amplitude Modulations: Vestigial Sideband (VSB)
VSB signals are relatively easy to generate, and their bandwidth is typically 25% greater than that of SSB signals.

## Slide 31: Demodulation of Vestigial Sideband (VSB)
-----------> 1
Substitute equation 1 and filter out spectra at ± 2 fc
M
| f |  B

## Slide 32: Demodulation of Vestigial Sideband (VSB)
For envelope demodulation, VSB+C require larger carrier than DSB+C but less than SSB+C.
Example: The carrier frequency of a certain VSB signals is fc = 20 kHz, and the baseband signal bandwidth is 6 kHz. The VSB shaping filter Hi(f) at the transmitter is shown below, find the filter H0(f) at the receiver for distortionless reception.

## Slide 33: Use of VSB in Broadcast Television
TV Broadcasting
Bandwidth 4.5 MHz
Has sizable power in the low-frequency region
Envelope detector is used instead of synchronous to reduce the cost of the receiver.
BW for SSB = 4.5 MHz
BW for DSB = 9 MHz
BW for VSB = 6 MHz

## Slide 34
Comparison among DSB, SSB, and VSB